## Slide 1: Electricity investment: Discrete choice modeling
Andrew Blohm

## Slide 2: Data
Dependent variable – weighted annual summer capacity addition for each unique prime mover and primary fuel pairing
  Form 860 – a survey of electric utilities that contains information down to the generator level
Capacity factor – calculated using the survey results from Form EIA-923, which contains information on technology choice, environmental compliance, net generation, etc.
  In this way we have capacity factors calculated specifically for the prime mover and primary fuel pairings unique to our study
Investment and variable cost – each annual energy outlook estimates the characteristics of new generating plants including operational characteristics and cost assumptions
  We weight the overnight cost by the capacity factor to standardize across production technologies
Fuel costs – EIA Electric Power Monthly report
  We use the generated heat rates to adjust for the efficiency of the production technology
Heat rate – a measure of efficiency in converting fuel into electricity. We calculate the average heat rate using Form 860, as well as the California energy almanac
More information on the data used and the data cleaning process can be found in the andymd26/fuzzy-waffle github repository

## Slide 3: Theory
An agent n faces a choice of technology alternatives J, j = 1, …, J
We assume that each agent is attempting to maximize their own utility U_{nj} through the selection of a technology alternative (i.e., each agent chooses a technology iff U_{ni} > U_{nj} i neq j
We can’t observe U_{nj}, instead we can observe information about the choice set x_{nj} for all j, as well as the agent s_{n} for all n
Using this information we can specify a utility function, where the specification of the error term depends on the researchers specification
  U_{nj} = V_{nj} + epsilon_{nj}, where V_{nj} = V(x_{nj}, s_{n})
The probability that agent n chooses technology j is
  Pr(epsilon_{nj} – epsilon_{ni} < V_{ni} – V_{nj} for all j neq i)
This is the probability that the difference in error terms is less than the difference in observed utility.
Pr(j | x) = integral(I(epsilon_{nj} – epsilon_{ni} < V_{ni} – V_{nj}) cdot f(epsilon_{n})d epsilon_n

## Slide 4: Model: multinomial logit
Logit parameterization makes the assumption that the unobserved portion of the density (f(epsilon_n)) is distributed iid extreme value for all i, which means that Pr(j | x) from the last slide simplifies to
  P_{ni} = e^V_{ni}/sum_j e^V_{nj}
The multinomial logit model assumes that
  The IIA assumption holds (i.e., unobserved portion of the utility is uncorrelated over the choice set and have the same variance)
  Another way to think about this is to consider the ratio of two alternatives, which should only depend on the characteristics of each alternative and not be related to other alternatives
  We could think of several reasons why this assumption might be violated in the electricity sector
Using the Hausman consistency test we reject the null hypothesis of IIA and thus, we should estimate the model with a structure that accounts for the violation of the IIA assumption.
The Hausman test checks that the probability ratio between each pair of choice alternatives is only determined by the characteristics of the alternative.

## Slide 5: Model: Nested multinomial logit
To address the violation of the IIA assumption we estimate a nested multinomial model using the same nesting structure found in GCAM.
The nests in GCAM are natural gas, coal, biomass, nuclear, refined liquids, solar, wind, and geothermal
GCAM estimates a model with an alternative specific constant and one elasticity for all of the nests.
Production technologies in our analysis (presently) include
  coal – steam turbine
  natural gas – combined cycle and combustion turbine
  Oil – combined cycle and combustion turbine
  Solar – photovoltaic and solar thermal
  Wind – onshore
  Geothermal
The nested logit model assumes that the error terms are distributed generalized extreme value (GEV), which allows for correlation among alternatives located in the same nest. The joint distribution of each nest now includes a new term tau_m that represents the correlation … and is often called the dissimilarity or inclusive value parameter).

## Slide 6: Results

## Slide 7: Discussion