## Slide 1: Electricity investment: Discrete choice modeling
Andrew Blohm

## Slide 2: Table of contents
Problem statement
Results
Discussion of the data
Theory
Methods

## Slide 3: Problem statement
In the electricity technology sector the logit parameters for the discrete choice model are not based on historical data, instead they represent a best guess.
a
The specification of the error (i.e., f(epsilon_n)) is what differentiates one discrete choice models from another. The current GCAM specification uses the Weibull distribution, while our specification uses the Generalized Extreme Value distribution (non-nested models use the extreme value distribution).
For this reason, we cannot directly compare the raw output of our model and the GCAM logit parameters. However, Robert using a Taylor series approximation found that if we divide the logit exponents used in the GCAM model by the fuel cost (we use the natural gas fuel cost) then we can compare the result with the model exponent.

## Slide 4: Results: Comparing the GCAM logit exponent to the multinomial logistic regression
 | Model logit exponent
 | -1.96
Fuel choice (i.e., nest) | GCAM logit exponent over cost
Coal | -1.61
Natural gas | -1.94
Oil | -1.09
Solar | -0.29
Geothermal | -0.74
Wind | -1.09
We can see that the current GCAM logit exponent parameterization is supported by the historical data.

## Slide 5: Data
Overnight cost – EIA overnight cost assumptions
Fixed and variable maintenance costs
Installed capacity – EIA Form 860
Heat rate
Fuel cost
Capacity factor
More information on the data used and the data cleaning process can be found in the andymd26/fuzzy-waffle github repository

## Slide 6: Data: Overnight cost (AEO)
The overnight cost is the cost of a construction project with no interest incurred.
Overnight cost data is available beginning in 1997 and is published every year. The categories of production technologies in each year has changed somewhat as old technologies are retired and new technologies emerge.
We use the overnight cost data from the supplemental materials found in each Annual energy outlook.
Each annual energy outlook estimates the characteristics of new generation units including operational characteristics and cost assumptions.
Each year the AEO estimates project lead time, average size, heatrate, fixed and variable operation and maintenance costs, and overnight costs for a suite of first and nth of its kind power production technologies.
Unfortunately, these categories do not match up well with the categories found in EIA form 860.

## Slide 7: Data: Fixed and variable maintenance costs (AEO)
From the AEO supplemental material we also select the fixed and variable operations and maintenance costs for each technology.
Fixed operations and maintenance costs are expenses that don’t vary with production (i.e., routine preventive and predictive maintenance, general and administrative expenses, etc.)
Variable operation and maintenance costs are expenses that vary with production such as water, disposal expenses, power purchases, etc.

## Slide 8: Data: Installed capacity (EIA Form 860)
Form 860 is a survey of electricity generators and is used to collect generator level data on existing and planned power plants with an installed capacity greater than 1 MW.
The dataset includes capacity, installation date, operating status, primary fuel, and technology at the generator, plant and utility level.
However, the technology categories in Form 860 do not readily map onto the overnight cost, technology categories. Thus, it requires mapping the available generator type in the overnight cost database to the installed capacity by generator in Form 860. We discuss these methods in our supplemental material.
Form 860 has 37 prime movers and 78 primary fuels, which form 190 unique, pair-wise combinations in the database, whereas the overnight cost database contains between 15 and 20 cost categories with the exact number fluctuating year-to-year.

## Slide 9: Data: Heat rate (various data sources)
The marginal cost of producing power not only depends on the price of fuel but also on the efficiency of the production process. The heat rate is a commonly used measure to assess the efficiency of a power plant in turning fuel into electricity.
Form 860 has generator level heat rate data for the period 1990 to 1995.
In July of 2007 the California Energy Commission adopted the Quarterly Fuel and Energy Report (QFER) requirement, which provided for the collection of information concerning electricity generation. The energy almanac contains plant level heat rate data for the period 2007 to present for all generators located in the state (Form 860 has data one level lower (i.e., the generator), whereas QFER is an average of the generators for a plant). Data in California actually begins much earlier in 2001.
We use a simple linear regression model to identify any trends in heat rate and project it forward.

## Slide 10: Data: Fuel cost
Fuel costs data are published in the Electric Power monthly report, which publishes the electric utility receipts and average cost for fossil fuels used in the power generation sector.
We adjust the fuel price for the efficiency of each production technology using the heat rate (i.e., new variable is the amount of fuel required to produce 1 MWh of electricity production).

## Slide 11: Capacity factor (Form EIA-923)
We calculate the capacity factor for each prime mover, primary fuel pairing using EIA Form 923.
EIA Form 923 surveys approximately 4,100 power plants each year and contains plant level data (i.e., one level above the generator) on technology choice, environmental compliance, net generation, etc.
We use the annual net generation found in Form 923 and the size found in EIA Form 860 to calculate the capacity factor, which necessarily introduces some error into our calculations (the two data sources do not agree on the number of generators at each site).
The advantage of this approach is that the capacity factors are tailored to our categories.

## Slide 12: Theory
An agent n faces a choice of technology alternatives J, j = 1, …, J
We assume that each agent is attempting to maximize their own utility U_{nj} through the selection of a technology alternative (i.e., each agent chooses a technology iff U_{ni} > U_{nj} i neq j
We can’t observe U_{nj}, instead we can observe information about the choice set x_{nj} for all j, as well as the agent s_{n} for all n
Using this information we can specify a utility function, where the specification of the error term depends on the researchers specification
  U_{nj} = V_{nj} + epsilon_{nj}, where V_{nj} = V(x_{nj}, s_{n})
The probability that agent n chooses technology j is the probability that the difference in error terms is less than the difference in observed utility.
a

## Slide 13: Model: multinomial logit
Logit parameterization makes the assumption that the unobserved portion of the density (f(epsilon_n)) is distributed iid extreme value for all i, which means that Pr(j | x) from the last slide simplifies to
  P_{ni} = e^V_{ni}/sum_j e^V_{nj}
The multinomial logit model assumes that
  The IIA assumption holds (i.e., unobserved portion of the utility is uncorrelated over the choice set and have the same variance)
  Another way to think about this is to consider the ratio of two alternatives, which should only depend on the characteristics of each alternative and not be related to other alternatives
  We could think of several reasons why this assumption might be violated in the electricity sector
Using the Hausman consistency test we reject the null hypothesis of IIA and thus, we should estimate the model with a structure that accounts for the violation of the IIA assumption.
The Hausman test checks that the probability ratio between each pair of choice alternatives is only determined by the characteristics of the alternative.

## Slide 14: Model: Nested multinomial logit
To address the violation of the IIA assumption we estimate a nested multinomial model using the same nesting structure found in GCAM.
The nests in GCAM are natural gas, coal, biomass, nuclear, refined liquids, solar, wind, and geothermal
GCAM estimates a model with an alternative specific constant and one elasticity for all of the nests.
Production technologies in our analysis (presently) include
  coal – steam turbine
  natural gas – combined cycle and combustion turbine
  Oil – combined cycle and combustion turbine
  Solar – photovoltaic and solar thermal
  Wind – onshore
  Geothermal
The nested logit model assumes that the error terms are distributed generalized extreme value (GEV), which allows for correlation among alternatives located in the same nest. The joint distribution of each nest now includes a new term tau_m that represents the correlation … and is often called the dissimilarity or inclusive value parameter).

## Slide 15: Discussion
Model could be expanded to include a correlation structure using the probit.
More data could be fed into the model (to take it further back in time to pick up more technologies.
…